YY-8015 luxury electronic treadmill

Please read all precautions and instructions in this manual before using this equipment.

Follow the principles of sustainable development, therefore may be necessary when the manual modifications and will not to notice, it’s all depending on the actual product.

Contents

Product  Brief              ………………………………………… 2

Security Precautions and Warnings   ……………………………………… 4

Installation Instructions            ……………………………………… 7

Using  instructions              ………………………………………11

Routine maintenance           …………………………………………13

1. Product Brief

B. Single electric treadmill:

| Main parameters and parts list |
| --- |
| Main technical parameters |
| No. | Parameters Names | Description |
| 1 | Input power voltage | AC220-240V(50/60Hz) |
| 2 | Motor power | 1.5HP |
| 3 | Speed | 0.8-14.8Km/h |
| 4 | Running surface | 1150*420 mm |
| 5 | Max user weight | 100KG |
| 6 | Expand dimensions | 1530*684*1160 mm |
| 7 | Functions (Option) | Running(disc plate,sit up,dumbbelland massage) |
| Packing list |
| No. | Name | units | Qty |  |
| 1 | Complete machine | set | 1 |  |
| 2 | Sit up up/dumbbells/massage | set | 1 |  |
| 3 | Accessory Bag | pc | 1 |  |
| 4 | Frame of Multi-function | pc | 1 |  |
| 5 | Frame pipe of Massager | set | 2 |  |
| Screws bag list |
| NO. | Name | QTY | NO. | Name | QTY |
| 1 | Inner Hexagon spanner 6mm | 1 | 8 | Audio cable | 1 |
| 2 | Inner Hexagon spanner 5mm | 1 | 9 | Safety key | 1 |
| 3 | Open spanner 13-15 | 1 | 10 | ScrewM8*45 | 2 |
| 4 | screwdriver | 1 | 11 | Screw M8*20 | 6 |
| 5 | Silicone oil | 1 | 12 | Screw M8 | 2 |
| 6 | manual | 1 | 13 | Flat washerφ8 | 2 |
| 7 | Arc gasketφ8 | 6 |  |  |  |

- Security Precautions and Warnings

:Please read the instructions carefully before use

- Indoor using and storing the treadmill, avoid dampness, and do not be spilled by water.

- Please wear suitable clothes and sneakers before exercise. Prohibited to exercise on the treadmill barefoot.

- High power plug must be grounded, electric outlet should have a dedicated circuit, do not share with other electrical equipment.

- Keep children away from the machine to avoid accidents.

- Avoid too long time and overload operation, otherwise will cause motor and controller damaged, and will accelerate wear of the bearing, running belt, running boards’ life time. Should maintain machine on a regular basis.

- Keep machine away from dust to avoid strong static.

- Please electric power off after using.

- Please maintain good ventilation when running.

- Please clamp security lock cable on your clothing to make sure safety off machine prevent at emergency condition.

- If you feel not very well when using this machine, please stop and consult a doctor.

- Silicone oil must keep children out of reach after use.

- If  power cord is damaged, please contact with qualified maintenance personnel for service rather than disassemble it at your own discretion.

Forbidden

- Don't use the machine in the status of the shell break in or break off （the internal structure exposed）or under the condition welding-parts may fall off.

---- Otherwise an accident or injury may be happened.

- Don't jump up and down in the process of movement.

---- may injury caused by the fall.

- Don't keep machine in or near moisture space such as the bathroom.

- Don’t place machine in direct sunlight, or high temperature places such as near stove and a heating appliance .

----Otherwise may cause the leakage and burst into flames.

- Don't use when the power cord damaged or power plug pin relaxation,

----otherwise will lead to get an electric shock, short circuit or fire.

- Don't damage or bent by force or reverse the power cord. Don’t place heavy objects on machine, don't clamp the power line.

----otherwise will cause fire or get an electric shock.

- Don't use machine more than 2 people at the same time, and don't  close to the machine when it is in use process.

---- or it may be an accident or injury due to falls.

- People can’t use the machine whom can’t express their consciousness or can’t operators by themselves.

----may occur accident or injury.

Person avoid drink water or pour water when operation.

---- may cause electric shock and fire. Forbidden!

- People who seldom do exercise shouldn't suddenly do intense exercise.

- When after eating or feel tired, do not use machine.

---- may lead to damage your health.

- This product is suitable for family use, does not apply to schools, gymnasium and so on. ---- There are the danger of injury.

- Don’t use when hard objects in pants pocket with.

----may cause accident or injury.

- Don’t use when the power plug on the needle, garbage, or water.

----may cause electric shock or short circuit, fire. Do not use with wet hand!

- when not in use, pull out the power plug from the socket.

----The dust and moisture can make the insulation aging, and result in leakage fire.

Ground protection system!

- This product must be grounded. If the machine is dysfunctional, grounding will provide good channel for electric current, in order to reduce the electric shock risk.

- This product is equipped the power of the equipment grounding conductor and grounding plug.Complete insert the plug to standard socket.

- If the equipment grounding conductor connection is improper, it will cause electrical shock. If you are have doubt about whether your product grounded correct or not, please entrust professional to check.

- Please this grounding plug’s shape, don’t Plug Adapter.

The range of movements and warm-up

Please suitable for your heart rate within the movement

warm-up with the soothing movement

A successful exercise program include warming up, aerobic exercise and slow movement .

The warm-up exercises is very important part and must be carried out before workout.

At the end of the movement repeat warm-up exercise can help alleviate muscle pain.

3. Installation Instructions

When installation, simple fixed all screws, shelf fully mounted after final tightening.

1. Put the machine flat on the ground.

2. Using Allen wrench 5# fix the column on the base by M8*45 lock washer and nut.

3. Holding left& right columns, use Allen wrench 5# to lock the Console frame on the columns by screw M8*20.

Above is a single function installation steps,

- Put two forms into the massage frame. Use tooling with M8*55 fix the screws on the massage frame.

NOTE: please confirm that all the above requirements unified lock all screws after installation, and check don’t have any left out before plug electricity.

* According to the physical, three levels for choose as below:

picture：1               picture：2               picture：3

4. Using  instructions

1.1  start-up

the normal start after 5 seconds of the countdown.

1.2 programming number

3 manually programmings, 12 automatically programmings, 1 FAT programming.

1.3 Safety lock function

Disconnect the security lock "E7" treadmill quick stop immediately, and with a Di tick alarm sound, put safety locks, electronic table full significant 2 seconds, all the data is cleared.

1.4 Key Functions

1.4.1 Start button, Stop button:

Start key, power on and press the “start” button, the speed display "0.8", treadmill starts work. Stop key, when treadmill in running state, press the “stop” button, all data is cleared, treadmill come to a complete stop and in the manual mode, the treadmill stops.

1.4.2. Program key:

Press “Program” button to choose manual mode or automatic program (P1 - P12); the default setting is manual mode , speed is from 0.8 km/h to 14.8km/h.

1.4.3 Setting key:

Three different countdown modes in standby mode: Time countdown mode, Distance countdown mode, and Calorie countdown mode; press speed plus and minus button to control the countdown value, after the setting is done, press the "Start" button to start the treadmill.

1.4.4 speed plus or minus key:

Adjust the speed of the treadmill, 0.1Km/press and automatic continuous increment or decremente keep press more than 2 seconds. Contains two buttons on the hand grip.

1.4.5 Speed shortcut keys:(without incline model)

Speed shortcuts the 1,3,5, 7,9,11 directly adjust the speed in running state.

1.4.6 窗体顶端

1.4.6 Multimedia control keys:

Play, pause, the former, the latter, the volume increase/decrease buttons. Play musics when insert U disc or SD card.

1.4.7 Touch keys.( this function only for the model with touch accessory)

PROG,  MODE,START,  STOP,SPD+, SPD- ,total 6 touch points.

1.4.8 Incline keys.( this function only for the model with incline)

3%、6%、9%  shortcuts. “

With the hands press the knob for the Start button, and more then press is the stop button, Clockwise rotation in the running for the speed , Counterclockwise to reduce the speed .

1.5 Display Function

1.5.1 Speed Display.

Display the currently running speed value.

1.5.2 Time Display

Display the manual mode, the running time or run-time mode and program countdown.

1.5.3 Distance display

Distance cumulative manual and program mode or the inverse distance mode.

1.5.4. Calorie display

Manual and program mode movement calories accumulated or calorie countdown mode.

1.5.5. Heart rate display

Heart rate signal is detected, the heart-shaped mark flashes while the pulse value.

1.5.6. Each window displays the range of the data:

TIME：5:00 – 99.59(MIN)

DISTANCE: 1.0 – 99.9(KM)

CALORIES: 20.0 – 999 (C)

SPEED: 0.8 – 14.8(KM/H)

PULSE: 50 – 199 (BPM)

1.6. Measured heart rate function

In the case treadmill energized, hold heartbeat piece heart rate shows that the initial value of the actual measured heart rate, the display range :50-200 times / min within 5 seconds. Heart-shaped graphics flashing test heartbeat process..

This data only just for reference, it can’t be considered as medical data.

1.7 Automatic program

Each program is divided into 10 segments, and the running time of the program of each program segment is evenly distributed. Following is a moving picture of the 12 programs.

| Program | set time / 10 = each time period set running time |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| P1 | SPEED | 3 | 3 | 6 | 5 | 5 | 4 | 4 | 4 | 4 | 3 |
| P2 | SPEED | 3 | 3 | 4 | 4 | 5 | 5 | 5 | 6 | 6 | 4 |
| P3 | SPEED | 2 | 4 | 6 | 8 | 7 | 8 | 6 | 2 | 3 | 2 |
| P4 | SPEED | 3 | 3 | 5 | 6 | 7 | 6 | 5 | 4 | 3 | 3 |
| P5 | SPEED | 3 | 6 | 6 | 6 | 8 | 7 | 7 | 5 | 5 | 4 |
| P6 | SPEED | 2 | 6 | 5 | 4 | 8 | 7 | 5 | 3 | 3 | 2 |
| P7 | SPEED | 2 | 9 | 9 | 7 | 7 | 6 | 5 | 3 | 2 | 2 |
| P8 | SPEED | 2 | 4 | 4 | 4 | 5 | 6 | 8 | 8 | 6 | 2 |
| P9 | SPEED | 2 | 4 | 5 | 5 | 6 | 5 | 6 | 3 | 3 | 2 |
| P10 | SPEED | 2 | 5 | 7 | 5 | 8 | 6 | 5 | 2 | 4 | 3 |
| P11 | SPEED | 2 | 5 | 6 | 7 | 8 | 9 | 10 | 5 | 3 | 2 |
| P12 | SPEED | 2 | 3 | 5 | 6 | 8 | 6 | 9 | 6 | 5 | 3 |

  - Body fat program is also useable for users.

Code Meaning of error messages

| Fault code | Failure Description | fault handling |
| --- | --- | --- |
| E1 | Communication Abnormal: when power on control and electronic communications under the exception. | Possible Cause: Electric and electronic communication is blocked, check each section of the spreadsheet to control communication connection, ensure that each core is fully plugged in. Check the meter and controller connection cable is damaged, replace the connection cable. |
| E2 | No speed sensor signal: output control voltage to DC motor under successive receives more than 3 seconds the motor speed feedback. | Possible Cause: Check the motor cable whether connected well and connect the motor wire again. Check the motor cable for damage have the smell and replace the motor. Check that the speed sensor is installed or damaged |
| E3 | Over current protection: in running, controlled under direct current motor is greater than the rated current detected over 6 a up to 3 seconds. | Possible Cause: More than the rated load causing excessive current, system of self-protection, the part is stuck treadmill, cause the motor to be transferred，Overloading, excessive current, systems to self-protection Adjust the treadmill power run it. There is check for liquid while motor is running or has a burned smell and replacement the motor; check that the controller is burnt smell and replace the controller; Or check the power supply voltage does not match the specifications , and using the correct voltage specification testing. |
| E6 | Explosion-proof impact protection: power supply voltage abnormality or damage cause abnormal motor drive motor circuit. | Possible Cause: Check that the power supply voltage is lower than normal voltage 50%，using the correct voltage specification testing again；check that the controller is burnt smell and replace the controller; Check the motor cable is connected and connect the motor wire again. |
| E7 | Without put the safety Key | Put the safety Key |

5. Routine maintenance

Warning: Before cleaning or maintenance products, please be sure the power plug of the treadmill is pulled out.

Cleaning: Comprehensive cleaning will extend the using life of the electric treadmill.

Removal of dust periodically in order to keep the parts clean. Be sure to clean running belt with both sides of the exposed portion, which will reduce the accumulation of impurities. Make sure that the clean athletic shoes, to avoid carrying the dirty matters into jogging board and belt. Treadmill belts shall be cleaned by a damp cloth with soap. And lease pay attention to avoid to wet the electrical components and running belt.

Make sure power plug disconnect before moving motor cover away, at least one time to clean motor every year.

This electric treadmill running board and running belt has been lubricated in factory. Friction between the running belt and running board have a great impact to the using life and the performance of the electric treadmill, therefore we subject to have a regular greasing. We recommend have a check on board regularly. If board surface is damaged, please contact our customer service center.

We recommend greasing electric treadmill running belt and running board following schedule:

Lightweight user (use less than 3 hours a week) once every 5 months;

Middleweight user (use 4-7 hours per week) once every 2 months;

Heavyweight use (use more than 7 hours a week) once every half month.

1.In order to better safeguard your electric treadmill and extend the life of the machine, it is recommended that your continued use one hours then off the power to make the machine rest for 10 minutes before use again.

2.If running belt is too loose, it will be slip; the belt too tight to reduce the motor performance and increase the roller, running belt more wear and tear.

The running belt should be better adjusted to make sure the treadmill in best condition.

Running Belt alignment

- Put electric treadmill on flat ground.

- Electric treadmill running at about 6-8km/hour speed.

- If the running belt is too far to the right, the direction of rotation of the right adjustment bolt clockwise 1/2 turn, then left adjusting bolt along the counter-clockwise 1/2 turn. Figure A

- If the running belt is too far to the left, the direction of rotation of to left adjusting bolt clockwise 1/2 turn, then 1/2 turn the right adjustment bolt counter-clockwise direction rotation. Figure B

Plus silicone oil

Step 1: First opened up the treadmill belt

Step 2: Open the silicone oil bottle, squeeze into the silicone oil in the running board side, as shown in the following Figure:

# 8. After-sales service

Thank you for using our treadmill, Products within normal use under one year, not the personal damaged, we allowing for a free repair or supply accessories. After expiry of the warranty we can provide repair parts and best prices. For more information please refer to the product warranty card.

Warranty card with each product by Dealer to fill in, Replacement parts for free during the warranty period, As a result of incorrect installation, improper used, Or change parts and cause  the malfunction, company shall not be liable. In addition, the warranty card issued by customers only for maintenance.

This product just only for household used not for business used, if this thing happened, our company will not be liable. If your product needs repair, please contact your local dealer.

# Text boxes

Safty key

Munal incline

Move wheel

Base frame

Display control table

Endcap

Long regular

Running belt

Motor cover

Handle heart rate

upright

Tips: Before folding the treadmill, make sure that the gradient of the "zero".

Notice:

!

!    Grounding instructions!